Cleaner Production and Ergonomics: a case of waste minimization and improvement of work conditions

Eduardo Concepción Batiz a, Salete Martins Alves b, Osnildo Gallo c, Antenor José de Souza d

a. Sociedade Educacional de Santa Catarina, Joinville, Santa Catarina, eduardo.batiz@sociesc.org.br

b. Sociedade Educacional de Santa Catarina, Joinville, Santa Catarina, salete.martins@sociesc.org.br

c. Sociedade Educacional de Santa Catarina, Joinville, Santa Catarina, galo@sociesc.org.br

d. Whirlpool, Joinville, Santa Catarina, jsantenor@yahoo.com.br

Abstract

This paper was made in thermal treatment area, in salt bath oven of an enterprise of North of Santa Catarina. Its goal was to determinate the factors that influence to waste generation of salt used in process. It was observed that mean cause of wastefulness is the position which the workers are obligated to adopt due to pre-determinate procedure, as well, the layout and tools used. The impossibility of workers maintains the workpiece draining of salt inside of oven, that due to weight, tool characteristics and the area conditions, causes an additional worker position problem. With direct observation technique, mo, filming, pictures and spaghetti diagram verified that due to layout the workers walk 430 m daily and this is one of the causes of salt quantity that is waster. This quantity is around 2.1 ton/year. With use of ergonomic and cleaner production principles were eliminated the detected problem of worker position, as well the unnecessary passage of workers and workpieces. It was proven the existence of strong synergy between ergonomic and cleaner production. Also both can be applied to improve the environment and to preserve the health, as well, to guarantee the workers safety.

Key words: Work conditions, Waste minimization, Cleaner production.