Cleaner Production Application in a Wood Industry in Amazon State

Bianca G. Pereira a, Ivan R. Neto b, Kaoru Yuyama a,

Hugo G. Pereira c e  Célio L. P. de Matos d

- Instituto Nacional de Pesquisas da Amazônia, Manaus-Am, bianca@inpa.gov.br e kyuyama@inpa.gov.br

- Universidade Católica de Brasília, Brasília-DF, ivan@pos.ucb.br

c. Kali-Umwelttechnik GmbH Sondershausen – Alemanha, Hugo.Galucio@k-utec.de

d. Serviço de Apoio às Micro e Pequenas Empresas do Amazonas, Manaus-AM, celio@am.sebrae.com.br

Abstract

This study shows the proposal of implantation of the Clear Production program (PmaisL) in a company Portela Industry and Commerce of Wood, located in Manaus-Am. Currently, the Portela company, wood floor producer for the external market, operate only with 25% of capacity, because their have difficulties for to acquire more legalized raw material. In current situation view, have been suggested practical of PmaisL with low costs, and Sebrae-AM subsidy at Technological Consulting Program, with economic and Environmental benefits. From the application of PmaisL methodos and on the basis of the identified chances, were opted to working with improvement of operational practical in the wood drying sector, for also having a direct relation with the quality control and for being the initial plant process, it is a basic process for the wood improvement. As intervention proposal, was created and used one accompaniment time-table of temperature and humidity that controlling and programmer the best time of drying, to be followed by an employee detached for this function. This measure generated a reduction of four days in the setting time/heater, with reduction of 1,4% in raw material with defect, 50% of water consumption in the heater, 25% of energy consumption, 25% of exploitation of residues in the ovens, diminishing in 25% of pollutant gases emission. Other generated benefits had been: generation of a new job; reduction of risks with burning equipment and accidents caused for the lack control and the time increase of the drier. The good acceptance of the PmaisL by the manager was attributed for any cost for the company, therefore the implemented action was gave for actions changes and insertion of procedures in the tasks application.

Keywords: Environment management, residues reduction in the source, good practical, wood company, Amazon.